## Slide 1
Review – 10/12/2020
Design A Robotic Arm
Presented by:
Saurabh Chopade- 99002716
Bhavesh Chavda- 99002715
Mentors:
Anand A T
Sandeep Talya

## Slide 2: Index
Problem Statement
Robot Terminology
Concept Generation
Concept Selection Matrix
Terminology and Interface Study (Roboanalyzer)
Material Selection
Sample Calculation and Result
Robot Arm Assembly
Static Analysis
Summary

## Slide 3: Problem Statement
Input Constraints | 
Robot arm type | RRP (2-Revolute and 1-Prismatic)
Maximum speed of arm | Max. speed up to 1m/s
No. of Axis | 3axis
Weight of Payload | Can lift 1kg
Maximum reach | 600mm
Design A Robotic Arm

## Slide 4: Robotics Terminology
Kinematics: The study of motion without regard to forces.
  Two types of Kinematics,
    Forward Kinematics : Input as angle between the link and we get output as co-ordinate of end effector.
    Inverse Kinematics : Input as co-ordinate of end effector and we get output as angle between the link.
Dynamics: The study of motion with regard to forces.
Workspace: The volume in space that a robot’s end-effector can reach, both in position and orientation.

## Slide 5: Concept Generation (1/2)
Revolute Joint 1
Revolute Joint 2
Prismatic Joint
Revolute Joint 1
Revolute Joint 2
Prismatic Joint
Concept 1
Concept 2

## Slide 6: Concept Generation (2/2)
Revolute Joint 1
Revolute Joint 2
Prismatic Joint
Concept 3

## Slide 7: Concept Selection
Parameter | Weightage | Concept 1 | Concept 2 | Concept 3
Speed | 5 | 3*5 | 3*5 | 2*5
Accuracy | 4 | 3*4 | 3*4 | 2*4
Lifting Capacity | 3 | 3*3 | 2*3 | 2*3
Up and Down Traverse | 2 | 3*2 | 1*2 | 3*2
Right and Left Traverse | 1 | 2*1 | 2*1 | 3*1
Total |  | 44 | 37 | 33
Property | Weightage
Best | 3
Better | 2
Good | 1

## Slide 8: Terminology and Interface Study (Roboanalyzer)
Forward Kinematics
Inverse Kinematics
Forward Kinematics output Matrix
Work Interface

## Slide 9: Material Selection (1/3)
Parameter | Weightage for parameter | Carbon Steel | Aluminum | ABS
Weight | 5 | 1*5 | 2*5 | 3*5
Strength | 4 | 3*4 | 2*4 | 1*4
Cost | 3 | 2*3 | 3*3 | 2*3
Manufacturability | 2 | 3*2 | 3*2 | 2*2
Corrosion Resistance | 1 | 3*1 | 3*1 | 3*1
Total |  | 32 | 36 | 32
Property | Weightage
Best | 3
Better | 2
Good | 1

## Slide 10: Material Selection (2/3)
Ashby Material Selection Chart

## Slide 11: Material Selection (3/3)
Ashby Material Selection Chart

## Slide 12: Sample Calculation and Result (1/6)
Prismatic Joint
Revolute Joint 1
Revolute Joint 2
L1
L3
L2
M1
M2
M3
M4

## Slide 13: Sample Calculation and Result (2/6)
Sr.No. | Component | Mass (Kg) | Length(mm)
1 | Link 1 | 0.59 | 150
2 | Link 2 | 0.913 | 250
3 | Link 3 | 0.42 | 200
4 | Motor 1 | 1.62 | -
5 | Motor 2 | 1.17 | -
6 | Motor 3 | 0.49 | -
7 | Gripper + Motor 4 | 0.6 | -
8 | Payload | 3 | -

## Slide 14: Sample Calculation and Result (3/6)
Torque for Motor 2
Mass of Motor =M
Mass of Link = m
Mass of Gripper = mg
Torque = {[(M4+mg) x (L2+L3 )] + [(m3) x (L3/2+L2)] + [(M3) x (L2)] + [(m2) x (L2/2)]} x g
= {(3.6 x 0.45) + (0.42 x 0.35) + (0.49 x 0.25) + (0.9 x 0.125)} x 9.81
Torque = 19.64 N.m
Torque for Motor 3
Torque = 7.5 N.m

## Slide 15: Sample Calculation and Result (4/6)
Torque = 0.22N.m
Torque Required = 0.22*FOS=0.66 N.m (Motor 1)

## Slide 16: Sample Calculation and Result (5/6)
Gripper Calculation
Friction Force Calculation
30N
N
f
Friction Force =
= 10 N
12N
29 mm
28.5 mm
F

## Slide 17: Sample Calculation and Result (6/6)
When gripper if fully open = 83.83°
F - 0.99F = 348
Hence,

## Slide 18: Robot Arm Assembly(1/3)
First Link
Middle Link
End Link
3 Finger Gripper
Motor 1
Motor 2
Motor 3
Motor 4

## Slide 19: Robot Arm Assembly(2/3)
Lead Screw
Roller Support
Slider
Lead Screw

## Slide 20: Robot Arm Assembly(3/3)
Coupling
Bush
Thrust Bearing
Base Plate
Floor Block
Support Column
Top Plate
Support Plate

## Slide 21: Static Analysis
Maximum deformation considering factor of safety
is 0.53mm
Maximum stress considering factor of safety
is 5.327e+06 N/m^2 < 2.75e+08 N/m^2 (Yield)

## Slide 22: Index & Mechanical Inputs
Index:
  Component Block Diagram
  Robot Arm Sketch and Isometric View
  Motor Selection List
  Sample Torque Calculation
  Motor Controller & Proximity Sensor Selection
Mechanical Inputs:
  Torque values for each motors
  Maximum operating speed

## Slide 23: Robot Arm Sketch
Prismatic Joint
Revolute Joint 1
Revolute Joint 2
L1
L3
L2
M1
M2
M3
M4

## Slide 24: Isometric View
First Link
Middle Link
End Link
3 Finger Gripper

## Slide 25: Component Block Diagram

## Slide 26: Motion Control-(Prismatic Joint)
Crouzet SQ57
BLDC Model | Crouzet SQ57
Part Number | 80280001
Operating Voltage | 12 – 36 VDC
Output Power | 82 W
Required Torque | 0.6 N-m
Torque achieved | 0.71 N-m
Base Speed | 1100 rpm (at 12 VDC)
Driver necessary | No
Encoder | Built-in (4096 resolution)
Weight | 1.62 kg

## Slide 27: Motion Control-(Revolute Joint 1)
Maxon DCX 35 L (Motor) + Gearhead + Controller + Encoder
DC Model | Maxon DCX 35 L, DC Graphite brushed
DC Part Number | DCX35L01GBKL434
Operating Voltage | 12 VDC
Output Power | 80 W
Base Speed | 7610 rpm (at 12 VDC)
Weight | 380 g
Torque Required/achieved | 22 N-m/24 N-m
Gearbox Model | Planetary Gearhead GPX 42 UP, 4 stage
Part Number | GPX42UPKLSL0243CPLW
Gear Ratio | 243:1
Maximum Torque | 35 N-m
Weight | 790 g

## Slide 28: Motion Control-(Revolute Joint 2)
Maxon EC-Max 30(Motor) + Gearhead + Controller + Encoder
BLDC Model | Maxon EC-max 30
BLDC Part Number | 272762
Operating Voltage | 12 VDC
Output Power | 60 W
Base Speed | 6590 rpm (at 12 VDC)
Weight | 300 g
Torque Required/achieved | 7 N-m/7.5 N-m
Gearbox Model | Planetary Gearhead GP 32 C, Ceramic version
Part Number | 166942
Gear Ratio | 86:1
Maximum Torque | 6 N-m
Weight | 190 g

## Slide 29: Motion Control-(Jaw)
Maxon DCX 32 L (Motor) + Gearhead + Controller + Encoder
DC Model | Maxon DCX 32 L, DC Graphite brushed
DC Part Number | DCX32L01GBKL448
Operating Voltage | 12 VDC
Output Power | 70 W
Base Speed | 6560 rpm (at 12 VDC)
Weight | 320 g
Torque Required/achieved | 0.5 N-m/0.54 N-m
Gearbox Model | Planetary Gearhead GPX 32, 1 stage
Part Number | GPX32AAKLSL05D3CPLW
Gear Ratio | 5.3:1
Maximum Torque | 1.25 N-m
Weight | 140 g

## Slide 30: Sample Torque Calculation for Revolute Joint 1
Mechanical Torque required (Tm) = 22 N-m (considering Safety Factor of 3)
Motor Output Power (Po) = 80 W
Motor Nominal Base Speed (No)= 7610 rpm
Gearbox Teeth Ratio (k) = 243:1
Speed after gearbox (N) = (No /k) = 7610/243 = 31.31 rpm
Nominal Electrical Torque Output = (60 * Po)/(2 * π * N) = 24.4 N-m > 22 N-m

## Slide 31: Motor Controller
ESCON Module 50/5
Controller Model | Maxon, ESCON Module 50/5
Part Number | 438725
Maximum Current | 15A
Operating Voltage | 10 – 50 VDC

## Slide 32: Proximity Sensor
Manufacturer | Autonics
Sensor Model | CR18-8DP
Sensor Type | Capacitive
Operating Voltage | 12-24 VDC
Sensing Distance | 8 mm
Response Frequency | 50 Hz
Response Frequency | 50 Hz

## Slide 33: Summary
Tasks Achieved:
  Selecting Motors based on Torque Requirements
  Selecting Controller & Encoder (feedback/sensing devices) for Closed loop control
  EMI/EMC Check
Task Remaining:
  Finalize micro-controller based on motor controlling demands
  PID Controller Calculation
  To create Load profile for all motors
  To select Power Supply adapter, connecting wires, connectors, etc.
  To prepare Bill Of Materials

## Slide 34
Thank You !